## Slide 1: Exam Questions
Dr. Zhixiang Zou

## Slide 2: Grid synchronization
Grid Synchronization in Power Converters
1. Single-phase grid synchronization
1.1. Describe the functionality and basic structure of a PLL.
1.2. Describe the structure of the PLLs based on in-quadrature signals (T/4 delay PLL, Park transform PLL, and SOGI-PLL have been introduced in both lecture and exercise).
1.3. Describe the features and the transfer functions of Second-Order Generalised integrator (SOGI).
2. Three-phase grid synchronization
2.1. Describe synchronization problems imposed by the unbalanced or distorted grid.
2.2. Describe the features of Decoupled Double Synchronization Reference Frame PLL (DDSRF-PLL). Describe and explain its response under unbalanced grid.
2.3. Describe the structure and advantages of DSOGI-Frequency-Locked Loop (DSOGI-FLL).

## Slide 3: Grid filter design and current control
1. Grid Filter Design
1.1. Describe the criteria of LCL filter design and the influence of sensor position.
1.2. Describe the resonance problem and damping solutions.
1.3. Describe the features and implementation of different active damping methods (multiloop method and filter-based methods have been introduced in both lecture and exercise).
2. Grid Current Control
2.1. Describe the grid current controls under synchronous and stationary frames.
2.2. Describe the design criteria of grid current control.
2.3. Describe the harmonic compensation schemes under synchronous dq frame (5th/7th harmonic compensation under dq frame and nested dq frame has been discussed in exercise).